## Slide 1: TRAFFIC LIGHTS MINI PROJECT
Embedded System (EE3427)

## Slide 2: Team Members
Dao Nguyen Khoi
2151215
2211208
Nguyen Dinh Huy
Nguyen Ha Phong Thinh
2151143

## Slide 3: TABLE OF CONTENTS 01 04 02 05 03 06
INTRODUCTIONS
REQUIREMENTS AND BOM
IMPLEMENTATION
FIRMWARE AND FLOWCHART
DEMONSTRATION
CONCLUSION

## Slide 4: INTRODUCTION 01

## Slide 5: INTRODUCTIONS
OVERVIEW
OBJECTIVES
Traffic light system includes 2 light poles that communicate wirelessly while supporting real-time synchronization
Automate intersection control, improve traffic flow efficiency, and minimize delays. It offers multiple operation modes to adapt to varying traffic conditions
Traffic congestion in urban areas requires adaptive solutions. This project showcases how embedded systems can enhance traffic management
MOTIVATION

## Slide 6: SYSTEM REQUIREMENTS AND BOM 02

## Slide 7: TRAFFIC LIGHTS REQUIREMENTS
ACTIVITY | KEY FEATURES | STATUS
Hardware | Adapter 9V to 5V via ASM1117, stable connections on breadboard | Done
Communication | HC-12 UART at 9600bps, channel 88, stable under 50m with noise | Done
Display | 16x2 I2C LCD, show real-time and mode, update every second | Done
Control | LED brightness varies depending on different mode via GPIO | Done
RTC | DS3231 via I2C, update every second via interrupt apply for automatic switching | Done
Mode Switching | 5 push buttons: Normal, Heavy, Night and Control mode | Done

## Slide 8: MODULE STM32
The STM32F103C8T6 includes multiple peripherals such as USART, SPI, I2C, and GPIOs, making it suitable for a traffic light system

## Slide 9: MODULE DS3231
A real-time clock (RTC) module provides accurate timekeeping. The module communicates via the I2C interface and battery backup for continuous operation during power loss

## Slide 10: MODULE LED 7 SEGMENT
A module led 7 segment with 74HC595 using SPI interface

## Slide 11: MODULE LCD & I2C
A 16x2 LCD using I2C peripherals with I2C module for easier display

## Slide 12: MODULE TRAFFIC LIGHT
A traffic light module is controlled by STM32 GPIO

## Slide 13: MODULE HC-12
A module using UART for wireless communication under 50 meters

## Slide 14: IMPLEMENTATION 03

## Slide 15: BLOCK DIAGRAMS
MASTER
SLAVE

## Slide 16: STM32 INTERNAL SCHEMATIC

## Slide 17: MASTER SCHEMATIC

## Slide 18
MASTER PCB

## Slide 19
MASTER PCB 3D

## Slide 20: SLAVE SCHEMATIC

## Slide 21
SLAVE PCB

## Slide 22
SLAVE PCB 3D

## Slide 23: FIRMWARE 04

## Slide 24: MASTER FLOWCHART
The flowchart provides an overview of how the Master works

## Slide 25: SLAVE FLOWCHART
The flowchart provides an overview of how the Slave works

## Slide 26: MODULE FIRMWARE

## Slide 27: SIMULATION 05

## Slide 29: CONCLUSION AND FUTURE DEVELOPMENT 06

## Slide 30
Limitation | Improvement Suggestion | Expected Enhancement
Communication limited to 50m and basic HC-12 module | Upgrade to LoRa module | Longer range communication
No traffic monitoring or violation detection | Add a surveillance camera with image processing to detect license plates and red-light violations | Enhance security, collect evidence of traffic violations
No response to emergency vehicles | Integrate a priority signal detection module (e.g., RF, LoRa, or sound detection) | Automatically adjust traffic lights for ambulances or police cars, reduce response time

## Slide 31: THANKS!
Do you have any questions?